## Slide 1: Thực hành mở rộng
ISIS Routing

## Slide 2: Content
ISIS Protocol
ISIS LAB
Q/A

## Slide 3: ISIS Routing Protocol
Intermediate System-to-Intermediate System (IS-IS) is a link state routing protocol
It uses Dijkstra’s SPF algorithm to choose routes (similar with OSPF)
It uses OSI protocols CLNS and CLNP to deliver its updates.

## Slide 4: NSAP Address Structure
Written in hexadecimal and have a maximum size of 20 bytes.
3 parts: the area ID, the system ID, and the NSEL
  Area IDs vary from 1 to 13 bytes
  The Cisco system ID must be exactly six bytes
  The NSEL is exactly one byte in size

## Slide 5: ISIS Levels
ISIS has a 2 layer hierarchy
  Level-2 (the backbone)
  Level-1 (the areas)
A router can be
  Level-1 (L1) router
  Level-2 (L2) router
  Level-1-2 (L1L2) router

## Slide 6: ISIS Levels
Level-1 router
  Has neighbours only on the same area
  Has a level-1 LSDB with all routing information for the area
Level-2 router
  May have neighbours in the same or other areas
  Has a Level-2 LSDB with all routing information about inter-area
Level-1-2 router
  May have neighbours on any area.
  Has two separate LSDBs: level-1 LSDB & level-2 LSDB

## Slide 10: Configuring IS-IS
Enable IS-IS on the router:
router(config)#router isis
Configure each router’s NET:
router(config-router)#net 49.0010.1111.2222.3333.00
Enable IS-IS on the router’s interfaces:
router(config)#interface s0/0/0
router(config-int)#ip router isis

## Slide 11: Configuring IS-IS
Set the IS level
router(config-router)is-type {level-1 | level 1-2 | level-2-only}
Set the circuit type on L1-2 routers
router(config-int)#isis circuit-type {level-1 | level 1-2 |level-2-only}

## Slide 14: Verifying and Troubleshooting
show isis topology: Displays the topology database and least cost paths.
show clns route: Displays the L2 routing table.
show isis route: Displays the L1 routing table. Requires that CLNS routing is enabled.
show clns protocol: Displays the router’s IS type, system ID, area ID, interfaces running IS-IS, and any redistribution.
show clns neighbors: Displays the adjacent neighbors and their IS level.
show clns interface: Displays IS-IS details for each interface, such as circuit type, metric, and priority.
show ip protocols: Displays the integrated IS-IS settings.

## Slide 15: Định tuyến VNPT NGN
UPE
UPE
UPE
UPE
UPE
Level-1 Area 30
Level-1 Area 20
Level-1 Area 10
MAN A
MAN B
MAN C
ISIS Level-1
PE-AGG
PE-AGG
SR
SR
ISIS Level-1-2
ISIS Neighbor
ISIS Backbone
ISIS Level-1 peer
ISIS Level-2 peer
ISIS Level-1-2
SR
SR
PE-AGG
Only Level-1 route here
ISIS Level-1-2 Peer

## Slide 16: ISIS LAB

## Slide 17: Q/A